## Slide 1
Objective Head-Related Transfer Function Evaluation Metrics for More Consistent Perceptual Assessment
Shanghao Zou | Supervisor: Dr. Baha Ihnaini
Department of Computer Science and Technology, Wenzhou-Kean University, Wenzhou, China
What is an HRTF?
Head-Related Transfer Functions (HRTFs) are acoustic filters encoding how an individual's anatomy (head, pinnae, torso) transforms sound — the cornerstone of binaural spatial audio over headphones.
Why Current Metrics Fail
• LSD is magnitude-only: completely blind to phase distortions.
• LSD is monaural: misses binaural cues (ILD, ITD) critical for spatial localisation.
• LSD is frequency-blind: weights all bands equally, obscuring critical pinna notches (4-12 kHz).
The "LSD Blindspot" - Key Motivation
Andreopoulou & Katz (2022) showed minimum-phase reconstruction achieves LSD < 1 dB ("perfect" by industry standards) yet caused subjective ranking collapse (r ~ 0.5) -- inverting assessments for ~18% of HRTFs.
Proposed Solution
A Composite Perceptual Metric (CPM) integrating LSD, ILD error, Group Delay error, and ITD error -- capturing both magnitude and phase degradations in a single weighted score.
Central Finding
Minimum-phase reconstruction achieves the LOWEST LSD (0.030 dB) of all conditions, yet produces the HIGHEST CPM (14.094) -- over 5x the next worst. This is the LSD blindspot empirically confirmed.
Results (mean +/- std, n = 20 subjects)
Condition LSD (dB) ILD Err (dB) GD Err (ms) CPM
Min-Phase 0.030 [*] 0.058 2.335 [*] 14.094 [*]
1/3-Oct Smooth 2.332 3.122 0.176 1.880
1/1-Oct Smooth 3.829 4.562 0.209 2.592
12-bit Quant. 0.140 0.238 0.060 0.352
8-bit Quant. 1.065 1.730 0.202 1.503
[*] = extreme value | GD weight = 0.35 (highest) -- phase-sensitive key discriminator
Key Observations
• Group Delay Error (2.335 ms) is 11-39x larger than any other condition -- directly exposing the phase destruction LSD cannot detect.
• CPM ranks all non-phase conditions monotonically (12-bit < 8-bit < 1/3-oct < 1/1-oct), confirming CPM retains full magnitude sensitivity.
• LSD vs. CPM scatter: min-phase sits at (LSD~0, CPM~14) -- far off the ideal diagonal -- while all other conditions cluster near it.
• Spectral plots (Figs. 3 & 4): magnitude spectra of original vs. min-phase are nearly identical (explaining low LSD), but group delay diverges massively in the pinna notch region (4-12 kHz).
Three Principal Contributions
1. LSD Blindspot Empirically Confirmed
Min-phase: LSD = 0.030 dB (best) yet CPM = 14.094 (worst). Direct empirical support for Andreopoulou & Katz (2022) on an independent database (RIEC vs. LISTEN).
2. Group Delay Error as Phase Discriminator
At 2.335 ms -- over 10x larger than any other condition -- GD error is the critical component that catches what LSD misses entirely.
3. CPM Captures Both Degradation Domains
CPM correctly ranks all five conditions -- detecting phase distortions while remaining monotonically sensitive to magnitude distortions.
Limitations
• No subjective listening tests; CPM-perception correlation unvalidated.
• CPM weights are heuristic (JND-based), not optimised against subjective scores.
• Only 20 of 51 available subjects used.
Future Work
▶ MUSHRA subjective validation (15 expert listeners, ITU-R BS.1534-3).
▶ SADIE II database cross-validation for generalisability.
▶ Empirical optimisation of CPM weights via regression against MOS.
▶ CPM as ML training loss function for HRTF generative models.
▶ Frequency-dependent weighting to emphasise pinna notch region (4-12 kHz).
Dataset: RIEC HRTF Database
• 20 subjects (10M / 10F); 865 spatial positions each; 512-sample HRIRs at 48 kHz (SOFA format)
• Analysis range: 200 to 16,000 Hz
5 Degradation Conditions
▶ A. Min-Phase Reconstruction -- preserves magnitude, destroys phase; ITD re-inserted.
▶ B. 1/3-Octave Smoothing -- mild spectral loss, phase intact.
▶ C. 1/1-Octave Smoothing -- aggressive; obliterates pinna notches.
▶ D. 12-bit Quantization -- noise floor ~-72 dB; minimal distortion.
▶ E. 8-bit Quantization -- noise floor ~-48 dB; clearly audible.
Four Metrics + CPM Composite
• Metric 1 -- LSD (dB): baseline magnitude metric.
• Metric 2 -- ILD Error (dB): binaural level difference; JND ~1 dB.
• Metric 3 -- Group Delay Error (ms): phase-sensitive key discriminator.
• Metric 4 -- ITD Error (ms): binaural timing; JND ~10-30 us.
CPM = 0.20*(LSD/2.0) + 0.25*(ILD/1.0) + 0.35*(GD/0.08) + 0.20*(ITD/0.03)
Weights reflect JND-based psychoacoustic thresholds. GD receives highest weight (0.35) to detect phase distortions LSD misses.
[1] Andreopoulou & Katz. Perceptual impact on localization quality evaluations of common pre-processing for non-individual HRTFs. JAES, 70(5):340-354, 2022.
[2] Gebru et al. A survey of advanced spatial audio research. arXiv:2508.10924, 2025.
[3] Armstrong et al. Perceptually enhanced spectral distance metric for HRTF quality prediction. JASA, 156(6):4133-4152, 2024.
[4] Panah et al. BINAQUAL: A full-reference objective localization similarity metric for binaural audio. arXiv:2505.11915, 2025.
[5] Ananthabhotla, Ithapu & Brimijoin. A framework for designing HRTF distance metrics that capture localization perception. JASA Express Letters, 1(4), 2021.
[6] Watanabe et al. RIEC HRTF Database, Tohoku University, 2014.
[7] Kistler & Wightman. A model of HRTFs based on PCA and minimum-phase reconstruction. JASA, 91(3):1637-1647, 1992.
[8] Zhang et al. Towards perception-informed latent HRTF representations. arXiv:2507.02815, 2025.
Introduction
Methods and Materials
Results
Conclusions
References